## Slide 1
S.T.Co-Op Education Society’s Science Senior College, Shahada
Operational Amplifiers
By: Asst. Prof. Anil Jagdale

## Slide 2
Index
Introduction
Background
Amplifier Introduction
Schematic of μA741
Characteristics of an Ideal Op Amp
Ideal versus Real Op-Amps
Applications

## Slide 3
Background
Originally invented in early 1940s using vacuum tube technology
  Initial purpose was to execute math operations in analog electronic calculating machines
Reduction in size with invention of transistor
Most now made on integrated circuit (IC)
  Only most demanding applications use discrete components
Large number of applications, low cost, and ease of mass production make them extremely popular

## Slide 4: Amplifiers
Single-ended Amplifier
Differential Amplifier
  Amplifies difference between inputs

## Slide 5
Schematic of μA741

## Slide 6
OpAmp Characteristics
Infinite voltage gain
Infinite input impedance
Zero output impedance
Infinite bandwidth
Zero input offset voltage (i.e., exactly zero out if zero in)

## Slide 7
Ideal versus Real Op-Amps
Parameter | Ideal Op-Amp | Real Op-Amp
Differential Voltage Gain | ∞ | 105 - 109
Gain Bandwidth Product (Hz) | ∞ | 1-20 MHz
Input Resistance (R) | ∞ | 106 - 1012 Ω
Output Resistance (R) | 0 | 100 - 1000 Ω
Ideal
Real

## Slide 8
Applications
Non-inverting Amplifier
Closed-loop voltage gain

## Slide 9
Unity-Gain Buffer
Closed-loop voltage gain
Used as a "line driver" that transforms a high input impedance (resistance) to a low output impedance.

## Slide 10
Inverting Amplifier
Current into op amp is zero

## Slide 11
Differential Amplifier
Current into op amp is zero

## Slide 13
Current-to-Voltage Converter