## Slide 1: Optimization algorithm
Sequencing models

## Slide 2: INTRODUCTION
A sequence is the order in which the jobs are processed. Sequence problems arise when we are concerned with situations where there is a choice in which a number of tasks can be performed. A sequencing problem could involve:
Jobs in a manufacturing plant.
Aircraft waiting for landing and clearance.
Maintenance scheduling in a factory.
Programmes to be run on a computer.
Customers in a bank & so-on.

## Slide 3: Terms used
Job : the jobs or items or customers or orders are the primary stimulus for sequencing. There should be a certain number of jobs say ‘n’ to be processed or sequenced.
Number of Machines : A machine is characterized by a certain processing capability or facilities through which a job must pass before it is completed in the shop. It may not be necessarily a mechanical device. Even human being assigned jobs may be taken as machines. There must be certain number of machines say ‘k’ to be used for processing the jobs.

## Slide 4: Continue...
Processing Time : Every operation requires certain time at each of machine. If the time is certain then the determination of schedule is easy. When the processing times are uncertain then the schedule is complex.
Total Elapsed Time : It is the time between starting the first job and completing the last one.
Idle time : it is the time the machine remains idle during the total elapsed time.
Technological order : different jobs may have different technological order. It refers to the order in which various machines are required for completing the jobs e.g.

## Slide 5: Where M1, M2, M3, M4 are machines.
FINISH
START
M4
M2
M3
M1

## Slide 6: Types of sequencing problems
There can be many types of sequencing problems which are as follows:
Problem with ‘n’ jobs through one machine.
Problem with ‘n’ jobs through two machines.
Problem with ‘n’ jobs through three machines.
Here the objective is to find out the optimum sequence of the jobs to be processed and starting and finishing time of various jobs through all the machines.

## Slide 7: Processing ‘n’ jobs through two machines
Let there be ‘n’ jobs each of which is to be processed through two machines say A & B, in the order AB. That is each job will go to machine A first and then to B in other words passing off is not allowed. All ‘n’ jobs are to be processed on A without any idle time. On the other hand the machine B is subject to its remaining idle at various stages.
Let A1 A2………….An & B1 B2……..Bn be the expected processing time of n jobs on these two machines.

## Slide 8: Continue…
Step 1. Select the smallest processing time occurring in list Ai or Bi, if there is a tie select either of the smallest processing time.
Step 2. If the smallest time is on machine A, then place it at first place if it is for the B machine place the corresponding job at last. Cross off that job.
Step 3. if there is a tie for minimum time on both the machines then select machine A first & machine B last and if there is tie for minimum on machine A (same machine) then select any one of these jobs first and if there is tie for minimum on machine B among and select any of these job in the last.
Step 4. Repeat step 2 & 3 to the reduced set of processing times obtained by deleting the processing time for both the machines corresponding to the jobs already assigned.

## Slide 9: Continue...
Step 5. Continue the process placing the job next to the last and so on till all jobs have been placed and it is called optimum sequence.
Step 6. after finding the optimum sequence we can find the followings
Total elapsed time = Total time between starting the first job of the optimum sequence on machine A and completing the last job on machine B.
Idle time in machine A = Time when the last job in the optimum sequence is completed on Machine B – Time when the last job in the optimum sequence is completed on Machine A.

## Slide 10: Ques.: In a factory, there are six jobs to process, each of which should go to machines A & B in the order AB. The processing timings in minutes are given, determine the optimal sequencing & total elapsed time.
Jobs | 1 | 2 | 3 | 4 | 5 | 6
Machine A | 7 | 4 | 2 | 5 | 9 | 8
Machine B | 3 | 8 | 6 | 6 | 4 | 1

## Slide 11: Continue...
Solution: step 1:the least of all the times given in for job 6 in machine B. so perform job 6 in the end. It is last in the sequences. Now delete this job from the given data.
Step 2: Of the remaining timings now the minimum is for job 3 on machine A. so do the job 3 first. Now delete this job 3 also.
Step 3: Now the smallest time is 3 minutes for job first on machine B. thus perform job 1 at the second last before job 6.
 |  |  |  |  | 6
3 |  |  |  |  | 6
3 |  |  |  | 1 | 6

## Slide 12: Continue...
Step 4: after assigning job 1, we observe that the smallest value of 4 minutes is shared by job 2 on Machine A and job 5 on machine B. so perform job 2 first and job 5 in at the end end, i.e. job 2 after job 3 and job 5 before job 1.
Step 5: now the only job remaining is job 4 it shall be assigned the only space left in the sequence. Optimal resultant sequence of jobs is
3 | 2 |  | 5 | 1 | 6
3 | 2 | 4 | 5 | 1 | 6

## Slide 13: The total elapsed time T is obtained as under:
Job Sequence |  |  | Machine A |  | Machine B |  | Idle time for machine B
 | MaC a | MAC B | IN | OUT | IN | OUT | 
3 | 2 | 6 | 0 | 2 | 2 | 8 | 2
2 | 4 | 8 | 2 | 6 | 8 | 16 | -
4 | 5 | 6 | 6 | 11 | 16 | 22 | -
5 | 9 | 4 | 11 | 20 | 22 | 26 | -
1 | 7 | 3 | 20 | 27 | 27 | 30 | 1
6 | 8 | 1 | 27 | 35 | 35 | 36 | 5

## Slide 14: Total Idle time for machine A is 1 minute (36-35) and for machine B is 2+1+5=8 minutes.

## Slide 15: Thank you