## Slide 1: S.Y.Biotechnology BT 302-Bioprocess Technology
Presented by
Pradnya V. Dhivare
(Dept. of Biotechnology)

## Slide 2: Introduction to Bioprocess Technology
Concept of Bioprocess Technology:
Bioprocess is any process that uses complete living cells or their components (e.g., bacteria, enzymes, chloroplast) to obtain desired products.
This process is commonly referred to as Fermentation.

## Slide 3: Range of Bioprocess Technology
There are five major group of commercially important fermentation-
1) Microbial Bioprocess
2) Microbial Enzymes
3) Microbial Metabolites
4) Recombinant Product
5) Transformation process

## Slide 4: Chronological Development
The Chronological development of Bioprocess Technology may be represented as:
Stage 1 - Pre -1900
Stage 2 - 1900 – 1940
Stage 3 - 1940 to present
Stage 4 - 1964 to present
Stage 5 - 1979 to present

## Slide 5: Basic Principal Component of Fermentation Technology
1) Drive motor , Heaters, Pump etc.
2) Vessels and Accessories
3) Peripheral Equipment (reagent bottle)
4) Instrumentation & Sensor

## Slide 6: Screening of Industrially Important Microorganism
Primary Screening :
Primary screening may be defined as detection and isolation of the desired microorganism based on its qualitative ability to produce the desired product like antibiotic or amino acid or an enzyme etc. In this process desired microorganism is generally isolated from a natural environment like soil, which contains several different species.

## Slide 7
The following are some of the important primary screening techniques:
(i) The crowded plate technique
(ii) Indicator dye technique
(iii) Enrichment culture technique
(iv) Auxanographic technique
(v) Technique of supplementing volatile and organic substrates.

## Slide 8: Crowded Plate Method
For screening of antibiotic producing organisms, the simplest technique is “crowded plate” procedure.
This technique is used where one is interested only in finding microorganisms that produces an antibiotic irrespective of its action against any specific organism. Hence, the sample is diluted only to such an extent that agar plates prepared from these dilutions will be crowed with individual colonies on agar surface. Colonies producing antimicrobial activity are indicated by clear zone of growth inhibition surrounding the colony.

## Slide 9
Secondary Screening
In primary screening, we detect and isolate the desired organism but in secondary screening, we characterize industrially important micro-organism which is isolated in primary screening by using highly selective procedures.
Here in secondary screening, we screen the organism that is capable of giving the high yield of the product by using the cheap raw material.

## Slide 10: Strain Improvement
Strain improvement is aTechnology of manipulating & improving microbial strains in order to enhance metabolic capabilities.
The directed improvement of product formation or cellular properties through modifications of specific biochemical pathways or by introduction of new pathways using recombinant DNA technology.

## Slide 11: Method of Strain Improvement
1) Genetic Recombination or Gene Transfer
2) Mutation
3) Genetic Engineering

## Slide 12: Working & Principle of culture collection center
Culture collections are centers that provide authentic examples of organisms that can be grown or maintained in the laboratory; they normally have a public service role and can provide associated information and services.

## Slide 13: Method of Preservation of culture collection
1) Refrigeration
2) Paraffin Method
3) Cryopreservation
4) Lyophilisation

## Slide 14: National centre for culture collection
1) National Collection of Industrial Microorganisms (NCIM) is a national facility and microbial culture repository dedicated to isolation, preservation and distribution of authentic and industrially important microbial strains.
Established in 1951, the NCIM is one of the oldest biological resource centers holding especially industrially important microorganisms in the country.
Collection holding currently comprises almost 5000 items, including Bacteria, Fungi, Actinomycetes, Yeasts & Algae.

## Slide 15: MTCC
2) The Microbial Type Culture Collection and Gene Bank (MTCC)
A national facility established in 1986 is funded jointly by the Department of Biotechnology (DBT) and the Council of Scientific and Industrial Research (CSIR), Government of India. The MTCC, housed at the Institute of Microbial Technology (IMTECH), Chandigarh, has established itself as a distinguished culture collection centre for microbial resources in India.